## Slide 1
Area and Wirelength Optimization in VLSI Floorplanning
Using Stockmeyer, HPWL and Simulated Annealing Techniques
23BVD1006 M Ramya Sree
23BVD1030 R Sandhyaa,
23BVD1044 Tejasvini R,
23BVD1061 Jagarakshitha V
BEVD303L - CAD FOR IC DESIGN

## Slide 2
The main goal is to minimize the total chip cost by optimizing two key metrics:
Our approach implements and compares a hybrid flow of algorithms to achieve a globally optimal and physically constrained floorplan.
•
Chip Area: Reducing the physical silicon footprint to lower manufacturing costs.
•
Wirelength (HPWL): Minimizing interconnect lengths to reduce signal delay, power consumption, and improve performance.
Project Objective

## Slide 3
Stockmeyer Algorithm
A dynamic programming algorithm to find the minimal area for a slicing floorplan from a given Polish expression.
HPWL Model
Half-Perimeter Wirelength. A fast, efficient model to estimate the total interconnect wirelength cost.
Simulated Annealing
A stochastic optimization method to find a global minimum by exploring the solution space and escaping local minima.
Core Algorithms

## Slide 4
Based on the initial Polish expression: B3 B7 H B5 B1 V B8 B2 H V B4 V B6 V H
This direct translation results in a non-optimal layout with significant wasted space.
Step 1: Initial Floorplan (Before)

## Slide 5
The Stockmeyer algorithm is applied to find the optimal area configuration for the same slicing structure.
It intelligently rearranges blocks to minimize dead space and create a compact layout.
Inputs:
Set of Blocks
Possible Block Shapes
Polish Expression
Step 2: Stockmeyer Optimization (After)

## Slide 6
Floorplan Stage | Width (W) | Height (H) | Area (A = W × H)
Initial Floorplan | 15 | 12 | 180
Stockmeyer Optimized | 13 | 9 | 117
Results: Area Optimization

## Slide 7
Wirelength Optimization
Applying HPWL and Simulated Annealing (SA) to the Stockmeyer floorplan to reduce interconnect costs.
Inputs:
Block Dimensions
Netlist
Net1: B1, B3
Net2: B2, B4
Net3: B1, B2, B5
Net4: B3, B4, B5
Net5: B1, B4
FLOORPLAN OF HPWL MODEL (LOCAL MINIMA)

## Slide 8
Both the model is modified to enforce the Stockmeyer-generated boundary (W=13, H=9) as a fixed constraint.
This prevents the floorplan from expanding or contracting, ensuring a dimensionally consistent layout.
This result balances area compactness with wirelength reduction.
Final Stats:
•
HPWL LOCAL MINIMA :
•
HPWL GLOBAL MINIMA (SIMULATED ANNEALING):
SIMULATED ANNEALING
FLOORPLAN AFTER SIMULATED ANNEALING

## Slide 9
Optimization Stage | Wirelength (HPWL) | Total Cost (Area + HPWL)
Stockmeyer Floorplan | 37.00 | 154.00
HPWL + Stockmeyer(constrained) | 31.00 | 148.00
SA + Stockmeyer(constrained) | 33.50 | 150.50
Results: Wirelength Comparison

## Slide 10
Area Optimized: The Stockmeyer algorithm provides an excellent, area-efficient (35% reduction) starting point for the floorplan.
Problem Identified: Unconstrained HPWL and SA methods achieve low wirelength but are impractical as they violate physical design boundaries.
Optimal Solution: The Constrained HPWL model is the superior solution. It maintains the compact area from Stockmeyer while achieving significant wirelength reduction.
Final Takeaway: This hybrid pipeline ensures a dimensionally stable, area-efficient, and wirelength-optimized floorplan, which is critical for practical VLSI implementation.
Conclusion